CPU documentation
Documentation on the 8-bit risc CPU architecture
Erkka Kääriä
2017-2018

Table of contents

# General information

- 8bit registers, 16-bit addressing
- 4 general purpose registers, R1, R2, R3, R4
- Load/Store architecture
- Little endian
- Unsigned and signed (two’s complement) arithmetic
- Inspired by 6502, 8086 and ARM architecture

# CPU registers

- Four 8 bit general purpose registers, R1, R2, R3, R4
  - No limitations on usage, can be used as source and destination registers as desired
- 16-bit program counter
- 16-bit stack pointer
- 8-bit status register, containing following bits, starting from the least significant bit
  - Zero flag
    - Last operation resulted in zero being stored into the destination register
  - Negative Flag
    - Last operation resulted in negative number, when interpreted as signed value (most significant bit is set)
  - Carry/Borrow flag
    - Addition: Last operation resulted into value larger than 255, when result interpreted as unsigned value
    - Subtraction: a < b, for equation ‘result= a – b’
  - Overflow flag
    - Last operation resulted in arithmetic overflow; value could not be represented by using two’s complement.
      - When both source operands share a sign bit and result has different sign, overflow occurs
  - Interrupt Flag
    - Interrupts are enabled (non-maskable interrupts will ignore this flag)
  - Break flag
    - Interrupt was generated by using the INT opcode rather than from external source.
  - Auto-increment flag
    - Certain values are automatically incremented. See addressing mode documentation for more information
  - Fault flag
    - CPU fault was generated, such as division by zero.

All GP-registers are initialized to zero. Stack pointer is initialized to $200. Flags are zero except for the interrupt flag, which is set. Program counter is initialized with value $0.

# Behavior on powering on the CPU

The CPU will jump to address stored at current PC location.
# Interrupts

The CPU supports both non-maskable and maskable interrupts. Maskable interrupts are ignored if the interrupt-flag is not set. Non-maskable interrupts are never ignored.

## Interrupt vector

Interrupt vector is a vector of addresses, starting from memory address $0. The cpu will jump to these addresses upon interrupt. The addresses stored are 16-bit values, in little-endian format.

Vector description	Start Address
Reset vector	$0
Invalid opcode	$2
Divide error	$4
Divide overflow	$6

The system should set up the interrupt vector table during early initialization.

## Non-maskable interrupts

### Faults

The CPU generates faults under the following circumstances:

- Invalid instruction was found in the instruction stream
- Division by zero
- Division result is not representable by 8-bit value (-128/-1)

When fault condition is met, the CPU will jump to the address located in the interrupt vector table. The chosen vector depends on the fault. CPU will also set the fault flag in the status register. The fault routine must clear this flag upon successful completion of the routine.

If fault flag is set when CPU encounters a fault condition, CPU jumps to the address stored in the reset vector instead. All registers are initialized with their default values, except for the program counter which contains the address stored in the reset vector.

One additional cycle is required compared to generic interrupt behavior in order to set the fault status flag.

## Generic behavior on interrupt

The CPU pushes the program counter high and low bytes into the stack. This value points to the next instruction in the instruction stream. The CPU will then push the status flags into the stack. Interrupt flag is then cleared. CPU will then fetch the low and high bytes of the interrupt handler address from the interrupt vector table. This process takes 6 cycles (push pc: 2 cycles, fetch ivector: 2 cycles, disable interrupts: 1 cycle, push status flags: 1 cycle)

Return from interrupt (IRET) reverses this process, restoring status flags and the program counter from the stack.

# Addressing modes

## Load/Store addressing modes

### Immediate addressing

Used by LDR

LDR <dr>, <immediate>
where
- dr is the destination register
- immediate is an 8-bit constant value

Example:

LDR r2, #$F0
- Load value $F0 into register r2
  - r2 = $F0

### Absolute addressing

Used by LDR/STR

STR <address>, <sr>
where
- address is the destination address where the value is stored
- sr is the source register

Examples:

STR $1234, r3
- Store register r3 into memory address $1234
  - byte *ptr = $1234
    *ptr = r3

LDR <dr>, <address>
where
- dr is the destination register where value is stored
- address is the source memory address

Example:

LDR r4, $1234
- Load value from address $1234 and store it in register r4
  - byte *ptr = $1234
    r4 = *ptr

### Indexed absolute addressing

Used by LDR/STR

STR <address>, <sr>, <ir>
where
- address is the base destination address where the value is stored
- sr is the source register
- ir is the index register

Example:

STR $1234, r1, r2
- Store register r1 into memory address $1234 + r2
  - byte *ptr = $1234 + r2
    *ptr = r1

LDR <dr>, <address>, <ir>
where
- dr is the destination register where the value is stored
- address is the base source memory address
- ir is the index register

Example:

LDR r1, $1234, r2
- load value from $1234 + r2 into register r1
  - byte *ptr = $1234 + r2
    r1 = *ptr

If auto-increment flag is set, the value of the index register is incremented after each load/store

Examples:

r2 contains value $12
After execution of LDR $1234, r1, r2, register r2 contains value $13

r2 contains value $FF
After execution of LDR $1234, r1, r2, register r2 contains value $00

### Indirect addressing

Used by LDR/STR

STR <[address]>, <sr>
where
- 16 bit value read from [address, address+1] (little endian) is used as the destination address
- sr is the source register

Example:
Assume address $1234 contains $F0, and address $1235 contains $A4.

STR [$1234], r2
- Bytes read from $1234 and $1235 form the address $A4F0, which is the actual destination address where the value of register r2 is stored
  - byte **ptr = $1234
    **ptr = r4

LDR <dr>, <[address]>
where
- dr is the destination register
- 16-bit value read from [address, address+1] (little endian) is used as the source address from which the value to be stored is loaded from

Example:
Assume address $1234 contains $F0, and address $1235 contains $A4.

LDR r3, [$1234]
- Bytes read from $1234 and $1235 form the address $A4F0, from which the actual values is read. This value is stored into register r3.
  - byte **ptr = $1234
    r4 = **ptr

If auto-increment flag is set, the address store in [address, address+1] is incremented by one after each load/store.

Examples:

Assume address $1234 contains $F0, and address $1235 contains $A4. Auto-increment flag is set.
After execution of STR [$1234], r2, address $1234 will now contain $F1. $1235 remains unchanged.

Assume address $1234 contains $FF, and address $1235 contains $A4. Auto-increment flag is set.
After execution of STR [$1234], r2, address $1234 will now contain $00. $1235 now contains $A5.

## Register operation instruction addressing modes

### Register-Register addressing

Used by instructions ADD, SUB

OP <dr>, <sr1>, <sr2>
where
- dr is the destination register
- sr1 is source register 1
- sr2 is source register 2

Example:

ADC r1, r2, r3
- Add r2 and r3, store result in r1
  - r1 = r2 + r3

### Register-Immediate addressing

Used by instructions ADD, SUB

OP <dr>, <sr1> <immediate>
where
- dr is the destination register
- sr1 is the source register
- immediate is an 8-bit constant value

Example:

SUB r4, r2, #$5
- Subtract constant value 5 from r2, store result in r4
  - r4 = r2 - $5
### Extended register-register addressing mode

Used by multiplication and division operations.

OP <dr1>, <dr2>, <sr1>, <sr2>
where
- dr1 is the destination register 1. The high byte of the result is stored here when multiplying,
  remainder when dividing
- dr2 is the destination register 2. The low byte of the result is stored here when multiplying,
  quotient when dividing
- sr1 is source register 1
- sr2 is source register 2

Example:

IMUL r4, r3, r1, r2
- multiply r1 with r2 and store the result in r4:r3
  - r4:r3 = r1 * r2
DIV r4, r3, r1, r2
- divide r1 with r2 and store the remainder in r4 and quotient in r3.
  - r3 = r1/r2
  - r4 = r1 mod r2

### Extended register-immediate addressing mode

Used by multiplication and division operations.

OP <dr1>, <dr2>, <sr>, <immediate>
where
- dr1 is the destination register 1. The high byte of the result is stored here.
- dr2 is the destination register 2. The low byte of the result is stored here
- sr is the source register.
- immediate is a constant value

Example:

MUL r4, r3, r1, #$20
- multiply r1 with $20 and store the result in r4:r3
  - r4:r3 = r1 * $20

### Destination-source addressing mode

Used by instructions that do not require second operand, such as bitwise not.
OP <dr>, <sr>
where
- dr is the destination register.
- sr is the source register.

Example:

NOT r3, r2
- Perform bitwise not on value stored in r2, and store the result in r3
  - r3 = ~r2

## Other addressing modes

### Implicit addressing

Some instructions, such as instructions affecting CPU flags do not specify addressing mode. This is because the addressing used is implicitly selected by the instruction (such as targeting the cpu flags)

# Instruction encoding

First 6 bits of opcode determine the instruction. The two remaining least significant bits determine the instruction addressing mode. This means the CPU supports up to 64 instructions, with up to 4 addressing modes per instruction.

Register encoding as bit patterns:
r1 = 0b00
r2 = 0b01
r3 = 0b10
r4 = 0b11

## Encoding for immediate addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b01
Second byte
Destination or source register encoded in the two least significant bits. Rest of the bits are zero.
Third byte
Immediate value

Example:
LDR r3, #$F0
Opcode: 0x10
Immediate addressing mode bits: 0b00
Register encoding: 0b11

Encoding	First byte	Second byte	Third byte
Binary	0b0100 0000	0b0000 0011	0b1111 0000
Hexadecimal	0x80	0x03	0xF0

## Encoding for absolute addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b01
Second byte
Destination or source register encoded in the two least significant bits. Rest of the bits are zero.
Third byte
The low byte of the 16-bit address
Fourth byte
The high byte of the 16-bit address

Example:
LDR r1, $ABCD
Opcode: 0x10
Absolute addressing mode bits: 0b01
Register encoding: 0b01
Encoding	First byte	Second byte	Third byte	Fourth byte
Binary	0b0100 0001	0b0000 0001	0b1100 1101	0b1010 1011
Hexadecimal	0x41	0x01	0xCD	0xAB

## Encoding for indexed absolute addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b10
Second byte
Destination or source register encoded in the two least significant bits. Index register stored in the next two least significant bits. Remaining four bits are zero.
Third byte
The low byte of the 16-bit address
Fourth byte
The high byte of the 16-bit address

Example:
LDR r4, $ABCD, r2
Opcode: 0x10
Indexed absolute mode bits: 0b10
Destination register encoding: 0b11
Index register encoding: 0b01
Encoding	First byte	Second byte	Third byte	Fourth byte
Binary	0b0100 0010	0b0000 0111	0b1100 1101	0b1010 1011
Hexadecimal	0x42	0x07	0xCD	0xAB

## Encoding for indirect addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b11
Second byte
Destination or source register encoded in the two least significant bits. Rest of the bits are zero.
Third byte
The low byte of the 16-bit address that points to memory location with actual address
Fourth byte
The high byte of the 16-bit address that points to the memory location with actual address

Example:
LDR r3, [$ABCD]
Opcode: 0x10
Indirect mode bits: 0b11
Destination register bits: 0b10
Encoding	First byte	Second byte	Third byte	Fourth byte
Binary	0b0100 0011	0b0000 0011	0b1100 1101	0b1010 1011
Hexadecimal	0x43	0x03	0xCD	0xAB

## Encoding for implicit addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b00.

Example:
CLA
Opcode: 0x06

Encoding	First byte
Binary	0b0001 1000
Hexadecimal	0x18

## Encoding for register-register addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b00.
Second byte
Destination register encoded in the least significant bits. Source register 1 encoded in the following 2 bits. Source register 2 encoded in the following 2 bits. The two most significant bits are zero.

Example:
ADD r1, r4, r3
Opcode: 0x31

Encoding	First byte	Second byte
Binary	0b1100 0100	0b00101100
Hexadecimal	0xC4	0x2C

## Encoding for register-immediate addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b01.
Second byte
Destination register encoded in the least significant bits. The source register encoded in the following 2 bits. Remaining 4 bits are zero.
Third byte
Immediate value

Example:
ADD r3, r2, #$20
Opcode: 0x31

Encoding	First byte	Second byte	Third byte
Binary	0b1100 0101	0b0000 0110	0b0010 0000
Hexadecimal	0xC5	0x06	0x20

## Encoding for extended register-register addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b00.
Second byte
High byte destination register encoded in the least significant bits. The low byte destination register encoded in the following 2 bits. Source register 1 encoded in the following 2 bits. Source register 2 encoded in the remaining 2, most significant bits.

Example:
IMUL r1, r2, r3, r4
Opcode: 0x34

Encoding	First byte	Second byte
Binary	0b1101 0000	0b1110 0100
Hexadecimal	0xD0	0xE4

## Encoding for extended register-immediate addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b01
Second byte
High byte destination register encoded in the least significant bits. The low byte destination register encoded in the following 2 bits. Source register encoded in the following 2 bits. The two most significant bits are zero.
Third byte
Immediate value

Example:
MUL r1, r2, r3, #$29
Opcode: 0x35
Encoding	First byte	Second byte	Third byte
Binary	0b1101 0101	0b0010 0100	0b0010 1001
Hexadecimal	0xD4	0x24	0x29

## Encoding for destination-source addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b00
Second byte
The destination register encoded in the least significant bits. Source register encoded in the following 2 bits. The remaining bits are zero
Third byte
Immediate value

Example:
NOT r1, r2
Opcode: 0x23
Encoding	First byte	Second byte
Binary	0b1000 1100	0b0000 0100
Hexadecimal	0x8C	0x04

# Instructions

## ADC
Add with carry

Add two integers together, and store the result in the destination register. If carry flag is set before computation, one is added to the result.

Flags affected: Overflow, Negative, Carry and Zero
Opcode: 0x30

Addressing mode	Syntax	Cycles
Register-register	ADC r1, r2, r3	3
Register-immediate	ADC r1, r2, #$30	4

## ADD
Add without carry

Adds two integers together and stores the result in the destination register. Status of the carry flag is ignored during the computation.

Flags affected: Overflow, Negative, Carry and Zero
Opcode: 0x31

Addressing mode	Syntax	Cycles
Register-register	ADD r1, r2, r3	3
Register-immediate	ADD r1, r2, #$30	4

## AND
Bitwise and

Perform bitwise and between two integers and store the result in the destination register.

Flags affected: Zero, Negative
Opcode: 0x20

Addressing mode	Syntax	Cycles
Register-register	AND r1, r2, r3	3
Register-immediate	AND r1, r2, #$30	4

## ASL
Arithmetic shift left

Left shift integer by given amount, with zeroes shifted in from the right. Last bit to be shifted out is stored in the carry flag.

Flags affected: Zero, Negative, Carry
Note: Only the three least significant bits of the shift amount are considered. Effectively this means the shift amount is modulo 8 of the original amount. This instruction is identical to logical shift left and shares the instruction encoding; these two instructions exist for symmetry.

Opcode: 0x24

Addressing mode	Syntax	Cycles
Register-Register	ASL r1, r2, r3	3
Register-immediate	ASL r1, r2, #$03	4

## ASR
Arithmetic shift right

Right shift integer by given amount, with sign bit shifted in from the left. Last bit shifted out is stored in the carry flag.

Flags affected: Zero, Negative, Carry
Note: Only the three least significant bits of the shift amount are considered. Effectively this means the shift amount is modulo 8 of the original amount.
Opcode: 0x25

Addressing mode	Syntax	Cycles
Register-Register	ASR r1, r2, r3	3
Register-immediate	ASR r1, r2, #$03	4

## BCC
Branch on carry clear

## BCS
Branch on carry set

## BEQ
Branch on equal (Branch on zero)

## BNE
Branch on not equal (Branch on not zero)

## BNG
Branch on negative

## BOC
Branch on overflow clear

## BOS
Branch on overflow set

## BPO
Branch on positive

## CALL
Subprocedure call

## CLA
Clear autoincrement flag

Clears the autoincrement flag in the CPU status register.

Flags affected: autoincrement flag (cleared)
Opcode: 0x06

Addressing mode	Syntax	Cycles
Implicit	CLA	2

## CLC
Clear carry

## CLF

Clear fault flag

## CLI
Clear interrupt enable flag

## CLO
Clear overflow flag

## CMP
Compare value

## DEC
Decrement value

## DIV
Unsigned divide

Divide two unsigned integers and store the quotient and remainder into the specified result registers. Division by zero generates a fault.

Flags affected: Zero flag, negative flag (undefined), carry flag (undefined), overflow flag (undefined)
Faults: Division by zero
Note: Zero flag is set if result is zero (numerator is zero). Status of the negative, carry and overflow flags is undefined.
Opcode: 0x36

Addressing mode	Syntax	Cycles
Extended register-register	DIV r1, r2, r3, r4	61
Extended register-immediate	DIV r1, r2, r3, #$20	62

## IDIV
Signed divide

Divide two signed integers and store the quotient and remainder into the specified result registers. Division by zero generates a fault. Division, where quotient is not representable by 8-bit signed integer generates a fault. Remainder has the same sign than the numerator.

Flags affected: Zero flag, negative flag (undefined), carry flag (undefined), overflow flag (undefined)
Faults: Division by zero, result does not fit 8-bit register
Note: Zero flag is set if result is zero (numerator is zero). Status of the negative, carry and overflow flags is undefined.
Opcode: 0x37

Addressing mode	Syntax	Cycles
Extended register-register	IDIV r1, r2, r3, r4	65
Extended register-immediate	IDIV r1, r2, r3, #$20	66

## IMUL
Signed multiply

Multiply two signed integers and store the low and high byte of the result into the specified result registers.

Flags affected: Zero Flag, Negative Flag, Carry Flag, Overflow flag,
Note: Carry and overflow flags are set if the low byte value sign­-extended into 16-bit value does not match the 16-bit high:low value (sign_extend(low) != high:low), cleared otherwise. Zero flag set if both high and low byte are zero, cleared otherwise. Negative flag is set if the most significant bit of the high byte is set, cleared otherwise.

Opcode: 0x34

Addressing mode	Syntax	Cycles
Extended register-register	IMUL r1, r2, r3, r4	37
Extended register-immediate	IMUL r1, r2, r3, #$20	38

## INC
Increment value

## INT
Software Interrupt

## IRET
Return from interrupt

## JMP
Jump to address

## LDR
Load register

Value is loaded into destination register from memory.

Flags affected: Zero and negative flags
Opcode: 0x10

Addressing mode	Syntax	Cycles
Immediate	LDR r1, #$A0	3
Absolute	LDR r4, $ABCD	5
Indexed absolute	LDR r2, $ABCD, r1	6
Indirect	LDR r3, [$ABCD]	7/9*

*Load Indirect takes two more cycles if address autoincrement flag is set.

## LSL
Logical shift left

Left shift integer by given amount, with zeroes shifted in from the right. Last bit to be shifted out is stored in the carry flag.

Flags affected: Zero, Negative, Carry
Note: Only the three least significant bits of the shift amount are considered. Effectively this means the shift amount is modulo 8 of the original amount. This instruction is identical to arithmetic shift left and shares the instruction encoding; these two instructions exist for symmetry.

Opcode: 0x24

Addressing mode	Syntax	Cycles
Register-Register	ASL r1, r2, r3	3
Register-immediate	ASL r1, r2, #$03	4

## LSR
Logical shift right

Right shift integer by given amount, with zeroes shifted in from the left. Last bit shifted out is stored in the carry flag.

Flags affected: Zero, Negative, Carry
Note: Only the three least significant bits of the shift amount are considered. Effectively this means the shift amount is modulo 8 of the original amount.
Opcode: 0x25

Addressing mode	Syntax	Cycles
Register-Register	LSR r1, r2, r3	3
Register-immediate	LSR r1, r2, #$03	4

## MUL
Unsigned multiply

Multiply two unsigned integers and store the low and high byte of the result into the specified result registers.

Flags affected: Zero Flag, Carry Flag, Overflow flag, Negative flag (undefined)
Note: Carry and overflow flags are set if high byte is nonzero, cleared otherwise. Zero flag set if both high and low byte are zero, cleared otherwise. Status of negative flag is undefined after execution.

Opcode: 0x35

Addressing mode	Syntax	Cycles
Extended register-register	MUL r1, r2, r3, r4	34
Extended register-immediate	MUL r1, r2, r3, #$20	35

## MOV
Move value between registers

## NEG
Negates the value of the register

## NOP
No operation

## NOT
Bitwise not

Invert bits of the specified register and store result in destination register.

Flags affected: Zero, Negative
Opcode: 0x23

Addressing mode	Syntax	Cycles
Destination-Source	NOT r1, r3	3

## OR
Bitwise or

Perform bitwise or between two integers and store the result in the destination register.

Flags affected: Zero, Negative
Opcode: 0x21

Addressing mode	Syntax	Cycles
Register-register	OR r1, r2, r3	3
Register-immediate	OR r1, r2, #$30	4

## POP
Pop value from stack into GP-register

## POPF
Pop status flags from stack into status register

## PUSH
Push GP-register value into stack

## PUSHF
Push status flags into stack

## RET
Return from subprocedure

## RETI
Return from interrupt

## ROL
Rotate left

Rotate bits in register by specified amount. Bits that are shifted out from left are shifted in from the right.

Flags affected: Zero, Negative
Opcode: 0x27

Addressing mode	Syntax	Cycles
Register-register	ROL	3
Register-immediate	ROL r1, r2, #$30	4

## ROR
Rotate right

Rotate bits in register by specified amount. Bits that are shifted out from right are shifted in from the left.

Flags affected: Zero, Negative
Opcode: 0x28

Addressing mode	Syntax	Cycles
Register-register	ROR	3
Register-immediate	ROR r1, r2, #$30	4

## SAI
Set autoincrement flag

Sets the autoincrement flag in the CPU status register.

Flags affected: autoincrement flag (set)
Opcode: 0x07

Addressing mode	Syntax	Cycles
Implicit	CLA	2

## SEC
Set carry flag

## SEI
Set interrupt enable flag

## STR
Store register

Value in register is stored into memory.

Flags affected: None
Opcode: 0x10

Addressing mode	Syntax	Cycles
Absolute	STR r4, $ABCD	5
Indexed absolute	STR r2, $ABCD, r1	6
Indirect	STR r3, [$ABCD]	7/9*

*Load Indirect takes two more cycles if address autoincrement flag is set.

## SBB
Subtract with borrow

Subtract two integers and store the result in the destination register. Carry flag is treated as a borrow flag, and 1 is subtracted from the result if the flag is set.

Flags affected: Zero, Negative, Overflow, Carry
Opcode: 0x32

Addressing mode	Syntax	Cycles
Register-register	SBB r1, r2, r3	3
Register-immediate	SBB r1, r2, #$30	4

## SUB
Subtract without borrow

Subtract to integers and store the result in the destination register. Status of the carry flag is ignored during computation.

Flags affected: Zero, Negative, Overflow, Carry
Opcode: 0x33

Addressing mode	Syntax	Cycles
Register-register	SUB r1, r2, r3	3
Register-immediate	SUB r1, r2, #$30	4

## TEST
Test bit pattern

Perform binary and between the source values, modify flags, and discard the result.

## XOR
Bitwise exclusive or

Perform bitwise exclusive or between two integers and store the result in the destination register.

Flags affected: Zero, Negative
Opcode: 0x22

Addressing mode	Syntax	Cycles
Register-register	XOR r1, r2, r3	3
Register-immediate	XOR r1, r2, #$30	4