CPU documentation
Documentation on the 8-bit risc CPU architecture
Erkka Kääriä
2017-2018

Table of contents

# General information

- 8bit registers, 16 bit addressing
- 4 general purpose registers, R1, R2, R3, R4
- Load/Store architecture
- Little endian
- Unsigned and two’s complement arithmetics
- Inspired by 6502, 8086 and ARM architecture

# CPU registers

- Four 8 bit general purpose registers, R1, R2, R3, R4
  - No limitations on usage, can be used as source and destination registers as desired
- 16-bit program counter
- 16-bit stack pointer
- 8 bit status register, containing following bits, starting from the least significant bit
  - Zero flag
    - Last operation resulted in zero being stored into the destination register
  - Negative Flag
    - Last operation resulted in negative number, when interpreted as signed value (most significant bit is set)
  - Carry flag
    - Last operation resulted into value larger than 255, when result interpreted as unsigned value
  - Overflow flag
    - Last operation resulted in arithmetic overflow; value could not be represented by using two’s complement.
      - When both source operands share a sign bit and result has different sign, overflow occurs
  - Interrupt Flag
    - Interrupts are enabled (non-maskable interrupts will ignore this flag)
  - Break flag
    - Interrupt was generated by using the INT opcode rather than from external source.
  - Auto-increment flag
    - Certain values are automatically incremented. See addressing mode documentation for more information
  - Fault flag
    - CPU fault was generated, such as division by zero.
    - Fault code is pushed into the stack

All gp-registers are initialized to zero. Stack pointer is initialized to $200. Flags are zero with the exception of the interrupt flag, which is set.

# Addressing modes

## Load/Store addressing modes

### Immediate addressing

Used by LDR

LDR <dr>, <immediate>
where
- dr is the destination register
- immediate is an 8-bit constant value

Examples:

LDR r2, #$F0
- Load value $F0 into register r2
  - r2 = $F0

### Absolute addressing

Used by LDR/STR

STR <address>, <sr>
where
- address is the destination address where the value is stored
- sr is the source register

Examples:

STR $1234, r3
- Store register r3 into memory address $1234
  - byte *ptr = $1234
    *ptr = r3

LDR <dr>, <address>
where
- dr is the destination register where value is stored
- address is the source memory address

Examples:

LDR r4, $1234
- Load value from address $1234 and store it in register r4
  - byte *ptr = $1234
    r4 = *ptr

### Indexed absolute addressing

Used by LDR/STR

STR <address>, <sr>, <ir>
where
- address is the base destination address where the value is stored
- sr is the source register
- ir is the index register

Examples:

STR $1234, r1, r2
- Store register r1 into memory address $1234 + r2
  - byte *ptr = $1234 + r2
    *ptr = r1

LDR <dr>, <address>, <ir>
where
- dr is the destination register where the value is stored
- address is the base source memory address
- ir is the index register

Examples:

LDR r1, $1234, r2
- load value from $1234 + r2 into register r1
  - byte *ptr = $1234 + r2
    r1 = *ptr

If auto-increment flag is set, the value of the index register is incremented after each load/store

Examples:

r2 contains value $12
After execution of LDR $1234, r1, r2, register r2 contains value $13

r2 contains value $FF
After execution of LDR $1234, r1, r2, register r2 contains value $00

### Indirect addressing

Used by LDR/STR

STR <[address]>, <sr>
where
- 16 bit value read from [address, address+1] (little endian) is used as the destination address
- sr is the source register

Examples:
Assume address $1234 contains $F0, and address $1235 contains $A4.

STR [$1234], r2
- Bytes read from $1234 and $1235 form the address $A4F0, which is the actual destination address where the value of register r2 is stored
  - byte **ptr = $1234
    **ptr = r4

LDR <dr>, <[address]>
where
- dr is the destination register
- 16-bit value read from [address, address+1] (little endian) is used as the source address from which the value to be stored is loaded from

Examples:
Assume address $1234 contains $F0, and address $1235 contains $A4.

LDR r3, [$1234]
- Bytes read from $1234 and $1235 form the address $A4F0, from which the actual values is read. This value is stored into register r3.
  - byte **ptr = $1234
    r4 = **ptr

If auto-increment flag is set, the address store in [address, address+1] is incremented by one after each load/store.

Examples:

Assume address $1234 contains $F0, and address $1235 contains $A4. Auto-increment flag is set.
After execution of STR [$1234], r2, address $1234 will now contain $F1. $1235 remains unchanged.

Assume address $1234 contains $FF, and address $1235 contains $A4. Auto-increment flag is set.
After execution of STR [$1234], r2, address $1234 will now contain $00. $1235 now contains $A5.
## Arithmetic instruction addressing modes

### Register-Register addressing

Used by instructions like ADD, SUB

OP <dr>, <sr1>, <sr2>
where
- dr is the destination register
- sr1 is source register 1
- sr2 is source register 2
Examples:

ADC r1, r2, r3
- Add r2 and r3, store result in r1
  - r1 = r2 + r3

### Register-Immediate addressing

Used by instructions like ADD, SUB

OP <dr> <sr1> <immediate>
where
- dr is the destination register
- sr1 is the source register
- immediate is a 8 bit constant value

Examples:

SUB r4, r2, #$5
- Subtract constant value 5 from r2, store result in r4
  - r4 = r2 - $5

## Other addressing modes

### Implicit addressing

Some instructions, such as instructions affecting CPU flags do not specify addressing mode. This is because the addressing used is implicitly selected by the instruction (such as targeting the cpu flags)

# Instruction encoding

First 6 bits of opcode determine the instruction. The two remaining least significant bits determine the instruction addressing mode. This means the CPU supports up to 64 instructions, with up to 4 addressing modes per instruction.

Register encoding as bit patterns:
r1 = 0b00
r2 = 0b01
r3 = 0b10
r4 = 0b11

## Encoding for immediate addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b01
Second byte
Destination or source register encoded in the two least significant bits. Rest of the bits are zero.
Third byte
Immediate value

Example:
LDR r3, #$F0
Opcode: 0x10
Immediate addressing mode bits: 0b00
Register encoding: 0b11

Encoding	First byte	Second byte	Third byte
Binary	0b0100 0000	0b0000 0011	0b1111 0000
Hexadecimal	0x80	0x03	0xF0

## Encoding for absolute addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b01
Second byte
Destination or source register encoded in the two least significant bits. Rest of the bits are zero.
Third byte
The low byte of the 16-bit address
Fourth byte
The high byte of the 16-bit address

Example:
LDR r1, $ABCD
Opcode: 0x10
Absolute addressing mode bits: 0b01
Register encoding: 0b01
Encoding	First byte	Second byte	Third byte	Fourth byte
Binary	0b0100 0001	0b0000 0001	0b1100 1101	0b1010 1011
Hexadecimal	0x41	0x01	0xCD	0xAB

## Encoding for indexed absolute addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b10
Second byte
Destination or source register encoded in the two least significant bits. Index register stored in the next two least significant bits. Remaining four bits are zero.
Third byte
The low byte of the 16-bit address
Fourth byte
The high byte of the 16-bit address

Example:
LDR r4, $ABCD, r2
Opcode: 0x10
Indexed absolute mode bits: 0b10
Destination register encoding: 0b11
Index register encoding: 0b01
Encoding	First byte	Second byte	Third byte	Fourth byte
Binary	0b0100 0010	0b0000 0111	0b1100 1101	0b1010 1011
Hexadecimal	0x42	0x07	0xCD	0xAB

## Encoding for indirect addressing mode

First byte
Opcode stored in the 6 most significant bits, followed by bits 0b11
Second byte
Destination or source register encoded in the two least significant bits. Rest of the bits are zero.
Third byte
The low byte of the 16-bit address that points to memory location with actual address
Fourth byte
The high byte of the 16-bit address that points to the memory location with actual address

Example:
LDR r3, [$ABCD]
Opcode: 0x10
Indirect mode bits: 0b11
Destination register bits: 0b10
Encoding	First byte	Second byte	Third byte	Fourth byte
Binary	0b0100 0011	0b0000 0011	0b1100 1101	0b1010 1011
Hexadecimal	0x43	0x03	0xCD	0xAB

## Encoding for implicit addressing mode

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b00.

Example:
CLA
Opcode: 0x06

Encoding	First byte
Binary	0b0001 1000
Hexadecimal	0x18

## Encoding for register-register addressing

First byte
Opcode stored in the 6 most significant bits. The two least significant bits are 0b00.
Second byte
Destination register encoded in the least significant bits. Source register 1 encoded in the following 2 bits. Source register 2 encoded in the following 2 bits. The two most significant bits are zero.

Example:
ADD r1, r4, r3
Opcode: 0x31

Encoding	First byte	Second byte
Binary	0b1100 0100	0b00101100
Hexadecimal	0xC4	0x2C

# Instructions

## ADC
Add with carry

## ADD
Add without carry

Adds two numbers together and stores the result in the destination register. Status of the carry flag is ignored during the computation.

Flags affected: Overflow, Negative, Carry and Zero flags are set/cleared based on the result of the computation.
Opcode: 0x31

Addressing mode	Syntax	Cycles
Register-register	ADD r1, r2, r3	3
Register-immediate	ADD r1, r2, #$30

## AND
Bitwise and

## ASL
Arithmetic shift left

## ASR
Arithmetic shift right

## BCC
Branch on carry clear

## BCS
Branch on carry set

## BEQ
Branch on equal (Branch on zero)

## BNE
Branch on not equal (Branch on not zero)

## BNG
Branch on negative

## BOC
Branch on overflow clear
## BOS
Branch on overflow set

## BPO
Branch on positive

## CALL
Subprocedure call

## CLA
Clear autoincrement flag

Clears the autoincrement flag in the CPU status register.

Flags affected: autoincrement flag (cleared)
Opcode: 0x06

Addressing mode	Syntax	Cycles
Implicit	CLA	2

## CLC
Clear carry

## CLI
Clear interrupt enable flag

## CLO
Clear overflow flag

## CMP
Compare value

## DEC
Decrement value

## DIV
Unsigned divide

## IDIV
Signed divide

## IMUL
Signed multiply

## INC
Increment value

## INT
Interrupt

## IRET
Interrupt return

## JMP
Jump to address

## LDR

Load value from memory into register

Value is loaded into destination register, in a way specified by the addressing mode. The instruction supports immediate, absolute, indexed absolute and indirect addressing modes.

Flags affected: Zero and negative flags, based on the state of the destination register after instruction
Opcode: 0x10

Addressing mode	Syntax	Cycles
Immediate	LDR r1, #$A0	3
Absolute	LDR r4, $ABCD	5
Indexed absolute	LDR r2, $ABCD, r1	6
Indirect	LDR r3, [$ABCD]	7/9*

*Load Indirect takes two more cycles if address autoincrement flag is set.

## LSR

Logical shift right

## MUL
Unsigned multiply

## MOV
Move value between registers

## NEG

Negates the value of the register

## NOP

No operation

## NOT

Bitwise not

## OR

Bitwise or

## POP
Pop value from stack into gp-register

## POPF
Pop status flags from stack into status register
## POPS
Pop value from stack into stack pointer (little-endian)

## PUSH
Push gp-register value into stack

## PUSHF
Push status flags into stack

## PUSHS
Push stack pointer into stack (little endian)

## RET
Return from subprocedure

## RETI

Return from interrupt

## ROL

Rotate left

## ROR

Rotate right

## SAI
Set autoincrement flag

Sets the autoincrement flag in the CPU status register.

Flags affected: autoincrement flag (set)
Opcode: 0x07

Addressing mode	Syntax	Cycles
Implicit	CLA	2

## SEC
Set carry flag

## SEI

Set interrupt enable flag

## STR

Store register into memory

## SBC
Subtract with carry

## SUB

Subtract without carry

## TEST
Binary and the source values and throw away the result.

## XOR
Bitwise exclusive or